## Slide 1
SECTION 1
Novelty & Key Features
1/5
Smart Scan Strategy for Electronic Warfare
Smart Scan learns WHEN and WHERE to look in the spectrum — with no prior threat library — from its own hits and misses.
› Interval-censored timing inference A miss isn't a null event — a d-ms look that saw nothing eliminates a whole phase interval for every candidate period.
› Learned discrete period prior 96.2% of 128,252 real radar scan periods fall on just 22 values → after one catch, ~19 candidate return times, not a continuum.
› Two competing emitter models Periodic flash vs. Gilbert–Elliott on/off, arbitrated by Bayes factors — covers the 88% of real emitters that aren't clean periodic flashes.
› Value-per-unit-receiver-time index Unifies exploit / discover-new / resolve-timing on one scale, so a 5 ms and a 100 ms option are directly comparable.
› Micro dwell controller 5 ms search looks, extend-on-partial-pulse, stop-on-confirm → lock-out 60.2%→69.1%, first-catch time cut 30–35%.
› Anti-synchronization by design Golden-ratio dither in search mode — structurally immune to the lock-out that defeats fixed sweeps.
› Explainable by construction Every dwell decision logs the numbers that produced it — shown live in the demo's decision panel.
› Threat-aware priority (optional) Classifies emitter threat level from observed parameters alone; operator-selectable mission profile.
Design principle: don't ask ML to rediscover radar physics — model what is known, learn the parameters online, let learning handle the residue.

## Slide 2
SECTION 2
Technical Architecture
2/5
Smart Scan Strategy for Electronic Warfare
Closed loop: observe → associate → predict → score → schedule → learn
L0
RF Front-End
Antenna → tunable receiver → digitiser
L1
Signal Processing
Pulse detection (CFAR) → PDW extraction
L2
Deinterleaving
Gate on AoA/freq/PW → cluster into tracks
L3
Emitter Knowledge
Periodic + on/off model bank, undiscovered belief, learned priors
L4
Decision
Rate index, micro dwell controller, dither, staleness governor
L5
Learning
Online: timing posteriors, visibility κ | Offline: priors, tuning, residual RL
L6
Control & HMI
Operator priorities, decision explanations, C2/fusion interface
DECISION RULE
Value per unit receiver time:
I(c,d) =
[ exploit known emitters
+ discover new emitters
+ λ · information gain ]
÷ (dwell + retune cost)
TECH STACK
• Python 3.12 + NumPy — core index/predict
• Gymnasium + SB3 Double-DQN — ML comparator
• FastAPI backend · Next.js/React frontend
• pytest (20 tests) · seeded, replayable benchmark
Repo modules: primes/env (receiver+scenarios) · primes/predict (track models) · primes/policies/primes_lite.py (index) · api/main.py + web/ (demo)

## Slide 3
SECTION 3
Impact & Benefits
3/5
Smart Scan Strategy for Electronic Warfare
4.2×
more flashes intercepted vs.
open-loop sweep (real data)
69.8%
Smart Scan interception on real
Turing dataset scenarios
95%
lock-out emitters discovered
(raster: only 15%)
3.2×
faster time-to-first-catch
(lock-out: 55.7s → 17.2s)
HEADLINE BENCHMARK (610 runs, real dataset scenarios)
Scheme | Interception
Open-loop raster | 16.8%
Greedy bandit | 20.3%
Double-DQN | 15.3%
Smart Scan | 69.8%
Clairvoyant oracle (upper bound) | 84.8%
› Operational 4.2× more of the EM picture; blind spots eliminated; earlier warning; better PRI/scan estimates from more samples.
› Economic Zero new hardware — a software upgrade to fielded receivers; one artefact set deploys fleet-wide.
› Strategic Works without an imported threat library; priors refit locally; transparent, auditable AI (not black-box RL).
› Beyond defence Spectrum regulation, interference hunting, radio-astronomy RFI mitigation, general sensor scheduling.

## Slide 4
SECTION 4
Feasibility & Viability
4/5
Smart Scan Strategy for Electronic Warfare
Not a proposal — a working, tested prototype with measured results.
› 20 unit tests · 610-run multi-seed benchmark (95% bootstrap CIs)
› 1,008-run robustness sweep across P_d / P_fa conditions
› Validated on 11 real Turing dataset scenarios, not just simulation
› Smart Scan / oracle ratio stays 0.67–0.75 as detection probability drops 1.0→0.5
› ≤2-point interception loss up to ~23 false alarms/run
RESOURCE FEASIBILITY
• Dev compute: a laptop (benchmark ~45 min on 3 cores)
• Data: open, Apache-2.0 licensed, streamed (no bulk storage)
• Licences/cost: $0 — fully open-source stack
• Runtime target: ~10⁴ ops/decision → fits embedded CPU
PATH TO FIELDED CAPABILITY
Stage | Work | Effort
TRL 3–4 (now) | Algorithm + simulator + dataset validation + demo | Done
TRL 4–5 | Real deinterleaving, HW-in-loop (SDR), C++/ONNX port | 3–6 mo
TRL 5–6 | ESM suite integration, multi-receiver, trials | 6–12 mo
TRL 6+ | Multi-platform fusion, certification, field trials | 12+ mo
KEY RISK & MITIGATION
› Missed detections/false alarms Graceful degradation is measured, not assumed.
› Real deinterleaving imperfect Prototype assumes upstream ID; dataset benchmarks this gap directly.
› Embedded real-time budget Bounded per-decision cost by design; ONNX/C++ port path defined.

## Slide 5
SECTION 5
Links & References
5/5
Smart Scan Strategy for Electronic Warfare
PROJECT LINKS
• Repo: github.com/abhishek-pandey7/Smart-Scan-strategy-for-Electronic-Warfare
• Full architecture doc: docs/SMART_SCAN_FULL_ARCHITECTURE.md
• Live demo (local): localhost:3000/mission?scenario=lockout
REPRODUCE IT YOURSELF
pip install -r requirements.txt
pytest -q # 20 tests
python -m experiments.benchmark --seeds 10 # rebuild benchmark.json
uvicorn api.main:app --port 8000 # backend
cd web && npm install && npm run dev # demo UI
PRIOR ART WE BUILD ON
• Clarkson, Optimisation of periodic search strategies for ES, IEEE Trans. AES 2011 — lock-out theory
• Liu & Zhao, Indexability of restless bandits & Whittle index, IEEE Trans. IT 2010 — index paradigm
• Nakhleh et al., NeurWIN: Neural Whittle Index Network, NeurIPS 2021 — learned index roadmap
• ML-based Receiver Scheduling for ES (Double-DQN), IEEE Xplore 11310649 — our comparator baseline
• The Alan Turing Institute, Turing Synthetic Radar Dataset, arXiv:2602.03856 — validation data
Every figure in this deck is reproducible bit-for-bit from a seed — no number here is hand-picked.